--------------------------------------------------------------------------------
--
--   AM2901 Benchmark
--
-- Source: AMD data book
--
-- VHDL Benchmark author Indraneel Ghosh
--                       University Of California, Irvine, CA 92717
--
-- Developed on Nov 1, 1991
--
--------------------------------------------------------------------------------


The "mem" block (RAM) operation is controlled by three most significant bits 
( I8, I7, I6) in the instruction. Thus there are eight possible cases.

The test vectors in "tv_mem.vhdl" test the "mem" component in 
all modes of operation for each of the eight cases.

NOTE : The Aadd is just there for reading from memory locations.

----------------------------------------------------------

(1) Load F into RAM(Badd). Badd = 0

F <= "0111";        
I <= "010000000";
RAM0 <= 'Z';
RAM3 <= 'Z';
Aadd <= 0;   
Badd <= 0;

----------------------------------------------------------

(2) Load F into RAM(Badd) where Badd = 1

F <= "1001";        
I <= "011000000";
RAM0 <= 'Z';
RAM3 <= 'Z';
Aadd <= 0;           
Badd <= 1;

----------------------------------------------------------

(3) Do nothing

F <= "0000";         
I <= "000000000";
RAM0 <= 'Z';
RAM3 <= 'Z';
Aadd <= 1;             
Badd <= 0;

----------------------------------------------------------

(4) Do nothing

F <= "1111";  
I <= "001000000";    
RAM0 <= 'Z';
RAM3 <= 'Z';   
Aadd <= 0;
Badd <= 1;

----------------------------------------------------------

(5)  Down shift F and load that into RAM(Badd)
     with input 0.  Badd = 2.

F <= "1001";         
I <= "100000000";
RAM0 <= 'Z';
RAM3 <= '0';
Aadd <= 1;           
Badd <= 2;          

----------------------------------------------------------

(6) Down shift F and load that into RAM(Badd)
    with input 1.  Badd = 3

F <= "0111";        
I <= "100000000";
RAM0 <= 'Z';
RAM3 <= '1';
Aadd <= 0;          
Badd <= 3;          

----------------------------------------------------------

(7) Down shift F and load that into RAM(Badd)
    with input 0.  Badd = 4

F <= "1101";         
I <= "101000000";
RAM0 <= 'Z';
RAM3 <= '0';
Aadd <= 2;      
Badd <= 4;      

----------------------------------------------------------

(8) Down shift F and load that into RAM(Badd)
    with input 1.  Badd = 5

F <= "1101";         
I <= "101000000";
RAM0 <= 'Z';
RAM3 <= '1';      
Aadd <= 3;        
Badd <= 5;

----------------------------------------------------------

(9) Up shift F and load that into RAM(Badd)
    with input 0.  Badd = 2

F <= "0110";        
I <= "110000000";
RAM0 <= '0';
RAM3 <= 'Z';        
Aadd <= 4;          
Badd <= 2;

----------------------------------------------------------

(10) Up shift F and load that into RAM(Badd)
     with input 1.  Badd = 6

F <= "0000";        
I <= "110000000";
RAM0 <= '1';
RAM3 <= 'Z';    
Aadd <= 2;      
Badd <= 6;

----------------------------------------------------------

(11) Up shift F and load that into RAM(Badd)
     with input 0.  Badd = 7

F <= "1101";        
I <= "111000000";
RAM0 <= '0';
RAM3 <= 'Z';
Aadd <= 5;    
Badd <= 7;    

----------------------------------------------------------

(12) Up shift F and load that into RAM(Badd)
     with input 1.  Badd = 8

F <= "0010";         
I <= "111000000";
RAM0 <= '1';
RAM3 <= 'Z';
Aadd <= 6;      
Badd <= 8;       

----------------------------------------------------------