--------------------------------------------------------------------------------
--
--   Intel 8251 Benchmark -- Receiver
--
-- Source:  Intel Data Book
--
-- VHDL Benchmark author Indraneel Ghosh
--                       University Of California, Irvine, CA 92717
--
-- Developed on April 7, 92
--------------------------------------------------------------------------------

TESTING THE 8251 MODEL

 OVERALL TESTING STRATEGY 

 In testing the functionality of the "transmitter" process, we mainly 
 concentrate on testing its main operational modes :

 (1) Synchronous transmission
 (2) Asynchronous transmission

 Functional details peculiar to each mode are tested in each case, among 
 others.

 We try to test various ports and signals in both their complimentary forms
 (1 and 0) which is analogous to testing for "stuck-at" faults in synthesised
 hardware. 

*************************************
*				    *
* (1) Synchronous transmission mode *
*		  		    *
*************************************

  The strategy is to transmit complementary values of all data bits and parity
  bit at least once. Parity is tested for even and odd mode. Also test for
  no parity.

  To test Single-SYNC and Double-SYNC modes, we let the transmission buffer
  remain empty at some times so that SYNC character(s) are transmitted.
  In Single-SYNC mode, the transmitter is made to send the same SYNC1 
  character twice consecutively, to check Single SYNC operation.

  Both SYNC1 and SYNC2 are tested for complementary values of all data bits.

  These tests are performed for all character lengths ( 5, 6, 7, 8 bits).

**************************************
*	 			     *
* (2) Asynchronous transmission mode *
*		  		     *
**************************************

  The strategy is to transmit complementary values of all data bits and parity
  bit at least once. Parity is tested for even and odd mode. Also test for
  no parity.

  Check for start bit, appropriate number of stop bits at all baud rates.
  Test for all possible baud rates (1X, 16X, 64X)
  Test for all possible numbers of stop bits (1, 1.5, 2)

  These tests are performed for all character lengths ( 5, 6, 7, 8 bits).

 --------------------------------------------------------------------------

 FORMAT OF TEST-VECTORS IN "*.bits" FILE ( "bit_format" )

 In this file, the test vectors for the "transmitter" process of the 8251
 USART are stored in a format known as the"bit_format". These test vectors
 can be very easily converted to other HDL formats. I have a C program that
 converts them into VHDL format.

 The "bit_format" has the following characteristics :

 1) This file is line-oriented and there are three types of lines :-
     
      [a] Port Description Lines
      [b] Actual Test Vector Lines
      [c] Comment Lines.

 2) All comment lines (Type [c]) begin with a star (*). While translating
    these test vectors into some HDL format (e.g. VHDL), the initial comment 
    lines are ignored. All other comment lines are copied verbatim into the 
    HDL file.

 3) In lines of Types [a] and [b], the line has many fields corresponding to
    ports of the entity being tested. A colon (:) acts as a field-separator 
    between ports ( We will call it a port separator). Each such line must 
    end with a colon.

 4) There are three Port Description Lines ( Type [a] ). These lines come
    just after the initial comment lines ( of Type [c] ). The three lines
    (in the following order) are :-

      {I} Port Name Line : This line specifies the names of all ports of the
                           entity being tested. Port names are separated by a
                           colon. 
                           
                           The order in which the port names are specified is 
                           significant. In all other lines of Type [a] and [b],
			   information pertaining to specific ports must appear
			   in the same order with a colon as a port-separator.

			   All input ports are mentioned first, followed by
                           the output ports. Inout ports are mentioned both
                           as input as well as output ports.
	   
      {II} Port Direction Line : This line specifies the directions ( in, out,
       				 inout ) of the ports mentioned in the Port
           			 Name Line ( Line {I} ).
                           
      {III} Port Type Line : This line is related to the data type ( e.g. 
			     bit, bit-vector, integer etc.) of the ports 
                             mentioned in the Port Name Line ( Line {I} ).
			     This line is very specific to VHDL data type
			     declaration syntax and may not be relevant to
			     other HDL's. 

 5) The Actual Test Vector Lines (Type [b] ) contain the test vectors for the
    8251. 

    Each test vector line is equivalent to one clock cycle. 

    Values corresponding to ports are written in the exact order in which
    port names are mentioned in the Port Name Line ( Type [a], Line {I} ).
    In case we dont want to mention any value for a particular port in that
    line, we put in one or more dashes ( - ) in that position corresponding 
    to that port. Values are separated by the colon as a port-separator.

    Values in the input-port positions in Type [b] lines are assigned to the
    corresponding input port. Only the "clocking" is implicit in the
    translation process for each test vector and the clock ( "TxC_BAR")
    is not specifically mentioned among the input ports. 

    Values in the output-port positions in Type [b] lines are compared to the
    actual output values appearing at the corresponding output ports when we
    run the simulation. If these two values dont match, then an "Assert" 
    statement is generated to show that an error has been detected.

--------------------------------------------------------------------------

HOW TO ADD MORE TEST VECTORS

    More test vectors can be easily added simply by entering more lines in
    "bit_format" to the end of the file. These lines must be "Actual Test 
    Vector Lines ( Type [b] )". 

    "Comment Lines ( Type [c] )" may also be added, but those will not have
    any effect on simulation.

--------------------------------------------------------------------------

TRANSLATION FROM "bit_format" TO VHDL.

 In this directory, I have a C program called "trans_tx.c" that does this 
 translation.

 The following steps can be followed :-

  (i) Compile the translator file.
          "cc trans_tx.c -o trans_tx"

  (ii) Run the translation program by specifying an input and an output file.
          "trans_tx sytx.bits sytx.vhdl"
       This program accepts test vectors in "bit_format" from an input file
       (for example) "sytx.bits" and produces test vectors in VHDL format in
       output file "sytx.vhdl"