--------------------------------------------------------------------------------
--
--   DOCUMENTATION ON THE GREATEST COMMON DIVISIOR
--
-- Source : "Algorithmics" by Brassard and Bradley
--
-- author: Ted Lee
--         University Of California, Irvine, CA 92717
--         tedl@ics.uci.edu
--
--   Developed on Feb 19, 1992
--
--------------------------------------------------------------------------------

 OVERVIEW

 The gcd model described in this example consists of two 8-bit input ports, 
 one 8-bit output port, and a one-bit input port that enables the gcd model 
 when the value is low.

_______________________________________________________________________________

 PORTS

 It has the following ports :-
_______________________________________________________________________________
|  PORT    | TYPE | BIT   |                DESCRIPTION                        |
|	   |      | WIDTH |						      |
|==========|======|=======|===================================================|
| xi	   |  in  |  8    | Input x                                           |
|__________|______|_______|___________________________________________________|
| yi       |  in  |  8    | Input y                                           |
|__________|______|_______|___________________________________________________|
| ou       | out  |  8    | Output ou = gcd(xi, yi)                           |
|__________|______|_______|___________________________________________________|
| rst      |  in  |  1    | ou = gcd(xi, yi) only when rst = '0'              |
|__________|______|_______|___________________________________________________|

_______________________________________________________________________________

 OPERATION 

 The gcd model can be enabled by setting rst='0'. The output ou will be 
 evaluated as gcd(xi, yi) based on the input values of xi and yi. If rst='1',
 then the output will be evaluated to be "00000000".