--------------------------------------------------------------------------------
--
--   Traffic light Controller Benchmark -- Simulation vector documentation
--
-- Source: The model and test patterns were obtained from the Hardware C   
--         model written by R. Gupta (7/23/90) at Stanford.
--
-- author: Champaka Ramachandran
--         University Of California, Irvine, CA 92717
--         champaka@balboa.eng.uci.edu
-- 
-- Written on August 11th 1992
--
--------------------------------------------------------------------------------

------------------
Testing Strategy :
------------------

There exists 4 Tests that cross check the following sequence of events :

  Strategy 1 
  ----------

Init --> Cars and TimeoutL --> TimeoutS --> !Cars  --> TimeoutS 

-- Pattern #0
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '0';

-- Pattern #1
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '1';

-- Pattern #2
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '1';

-- Pattern #3
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '0';

-- Pattern #4
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '1';


          1. Checks whether the initial condition sets the Highway 
             light to green and the Farm light to red.
          2. Checks if there is a car on the side road and the long
             timeout occurs, the highway light changes to yellow.
          3. After a short time out the highway light changes to
             red and the farm light changes to green.
          4. If there are no cars on the side road, the farm light
             changes to yellow.
          5. After a short timeout, the farm light changes to red
             and the highway light changes to green.


  Strategy 2
  ----------

  Cars and TimeoutL --> !Cars --> TimeoutL --> Timeout L and TimeoutS


-- Pattern #5
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '0';

-- Pattern #6
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '0';

-- Pattern #7
Cars <= '0';
TimeoutL <= '1';
TimeoutS <= '0';

-- Pattern #8
Cars <= '0';
TimeoutL <= '1';
TimeoutS <= '1';


          1. Checks if there is a car on the side road and the long
             timeout occurs, the highway light changes to yellow.
          2. If there is no short timeout, then the Highway light 
             changes to red and the farm light changes to yellow.
          3. No change
          4. After a short timeout, the highway light changes to green
             and the farm light changes to red.


  Strategy 3
  ----------

  Cars -> Cars & TimeoutS --> Cars & TimeoutL --> Cars, TimeoutS & Timeout L
     --> Cars --> Cars & TimeoutL --> Cars and TimeoutS


-- Pattern #9
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '0';

-- Pattern #10
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '1';

-- Pattern #11
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '0';

-- Pattern #12
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '1';

-- Pattern #13
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '0';

-- Pattern #14
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '0';

-- Pattern #15
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '1';


          1. No Change.
          2. No Change.
          3. Checks if there is a car on the side road and the long
             timeout occurs, the highway light changes to yellow.
          4. After a short time out the highway light changes to
             red and the farm light changes to green.
          5. No change. 
          6. If there is a long time out, the farm light changes to yellow. 
          7. After a short timeout, the highway light changes to green
             and the farm light changes to red.
          8. No Change.

  Strategy 4
  ----------

-- Pattern #16
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '0';


-- Pattern #17
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '1';
wait for 10 ns;

-- Pattern #18
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '0';

-- Pattern #19
Cars <= '1';
TimeoutL <= '1';
TimeoutS <= '1';


-- Pattern #20
Cars <= '1';
TimeoutL <= '0';
TimeoutS <= '0';


-- Pattern #21
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '0';


-- Pattern #22
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '0';


-- Pattern #23
Cars <= '0';
TimeoutL <= '0';
TimeoutS <= '1';

Cars & TimeoutL --> Cars, TimeoutL & TimeoutS --> Cars --> None --> TimeoutS 

          1. Checks if there is a car on the side road and the long
             timeout occurs, the highway light changes to yellow.
          2. After a short time out the highway light changes to
             red and the farm light changes to green.
          3. No change. 
          4. If there are no cars on the side road, the farm light
             changes to yellow.
          5. After a short timeout, the highway light changes to green
             and the farm light changes to red.